## Slide 1
Tommaso Califano · Giovanni Ligato · Nicola Ramacciotti · Gabriele Suma
UNIVERSITÀ DI PISA
Master’s degree in Computer Engineering
Mobile and Social Sensing Systems
Marco Avvenuti · Alessio Vecchio
Sensing how consumers experience Food

## Slide 2
Setting the Table
Most dining experiences go unrecorded—people simply don’t have the time, interest, or motivation to write reviews.
Why Foodback?

## Slide 3
Yet every bite tells a story
Our goal is to capture that story—automatically.

## Slide 4
+
A mobile-based prototype that evaluates food experiences by analyzing brain and body signals. Bringing objectivity and automation to digital gastronomy.
What we Propose
No user input required

## Slide 5
Inside the Foodback Experience
Foodback
Foodback
Inside the Foodback Experience

## Slide 6
Splash Screen

## Slide 7
Login Screen
Login Made Simple
Users can access Foodback’s features quickly and securely using just their email and password—nothing more.

## Slide 8
No account? No problem.
You can easily register for Foodback anytime through the sign-up page.
Sign-Up Screen

## Slide 9
From Login to Evaluation
After logging in, users are directed to their main dashboard, where the pre-trained machine learning model is ready to evaluate tasting experiences automatically.
Evaluation Screen
Both the EEG cap and the smartwatch must be connected—indicated by green icons—before the app allows inference to proceed.

## Slide 10
The Secret Ingredient
If the logged-in user is an Admin, an alternate route is revealed. Instead of the standard dashboard, the Admin accesses a dedicated data collection interface, used to gather EEG and smartwatch signals for training the machine learning model.
This experimental page enables controlled sessions across multiple participants and will be detailed further in the protocol discussion.
Data Collection Screen

## Slide 11
SYSTEM ARCHITECTURE
Mobile Phone
EEG
MindRove ARC
Heart Rate
Electrodermal Activity
Smartwatch
Google Pixel Watch 2
Backend
Flask
Database
MySQL

## Slide 12
Companion Application
Splash Screen
Main Screen
Powered by WearOS

## Slide 13
Android Wearable API
Part of Google Play Services
Provides a communication channel between wearable devices and connected handheld devices
Message Client API is a part of the Android Wearable API that enables sending short, one-way, real-time messages between connected devices
WearOS
Android

## Slide 14
MINDROVE SDK
Mindrove SDK 2.0 for Android
SensorData:
            Channel[1-6]
        NumberOfMeasurements
        Voltage
The ServerManager class is responsible for managing a server thread and its interactions.

## Slide 15
TASTING PROTOCOL
  Device Initialization:
            The protocol begins once EEG and wearable watch (HR & EDA) are connected and ready to transmit data
            Preparation Phase (5 seconds):
              A first beep signals the subject to bring the food sample into the mouth
              This is a 5-second window to prepare for tasting
              Recording Phase (10 seconds):
              A second beep marks the start of data recording
              For the next 10 seconds, the system captures EEG, HR, and EDA signals, representing the subject’s sensorial response to the food
              Rating Phase:
              A final beep ends the data capture
              A rating interface appears for the administrator to input the subject's sensorial experience rating

## Slide 16
TASTING PROTOCOL (2)
Health check on devices status
Starting the protocol
Preparation phase of 5 secs
EEG and Wearable data recording phase of 10 secs

## Slide 17
TASTING PROTOCOL (3)
Rating the sensorial experience
Data collected and session completed
Manage your data in one-tap

## Slide 18
TASTING PROTOCOL
PREVIEW MODE
A complex protocol requires clear instructions
Identify and fix signal issues
How do we help subjects understand each step to optimize data quality?
Preview Mode
All steps are performed exactly as in the real session, but no data is saved
Train participants with full protocol exposure

## Slide 19
Data collected via the App in Admin mode:
Manages cues and rating input;
Streams EEG from MindRove Arc;
Triggers smartwatch HR and EDA recording;
Saves one CSV per sensor, preserving native sampling rates.
CSV Management
Our Homemade Dataset
Small but Gathered with Love
TOTAL TASTING SESSIONS
45
10
PARTICIPANTS
(ages 16–56)
A bottom sheet lets you delete or share CSV files individually, making it easy to export data for training after experiments.

## Slide 20
Pre-Processing
HR
EEG
EDA
Sampling Frequency
500 Hz
~1 Hz
~10 Hz
Upsampling
125 Hz
Upsampling
125 Hz
HOLD-OUT
SPLITTER
80/20
Split by Experiment
TRAINING SET
TEST SET
TRAINING SET
TEST SET
TRAINING SET
TEST SET

## Slide 21
What is an Epoch?
10 s
TASTING SESSION
=
5
2 s
SEGMENT
This is an Epoch
1 Experiment
5 Epochs
The epochs form the input units for the machine learning model.
INFO

## Slide 22
EEGNet
The Kitchen-Ready Classifier Adopted
Lawhern et al. (2018)
Compact CNN specifically designed for EEG.
Tiny two-layer footprint, ideal for small EEG datasets
Depthwise convolutions for learning spatial patterns.
TOTAL PARAMETERS
1861
TRAINABLE
1781
NON-TRAINABLE
80

## Slide 23
EMBEDDED EEG PRE-PROCESSING
All EEG pre-processing steps are fused directly into the TensorFlow model, so no external DSP or signal handling is needed on-device.
EPOCH
2 s
Foodback ML Model
PREDICTED RATING
TENSORFLOW GRAPH
Simplifies the deployment on Kotlin
Very few details

## Slide 24
EMBEDDED EEG PRE-PROCESSING
Foodback ML Model
TENSORFLOW GRAPH
HR
EDA
EEG
CH1
CH2
CH3
CH4
CH5
CH6
500 Hz
RAW
UPSAMPLED
125 Hz
UPSAMPLED
125 Hz
6 x 1000
SAMPLES
1 x 250
SAMPLES
1 x 250
SAMPLES
PREDICTED RATING
A bit more detail

## Slide 25
EMBEDDED EEG PRE-PROCESSING
TENSORFLOW GRAPH
A bit more of more detail
HR
EDA
EEG
CH1
CH2
CH3
CH4
CH5
CH6
500 Hz
RAW
UPSAMPLED
125 Hz
UPSAMPLED
125 Hz
6 x 1000
SAMPLES
1 x 250
SAMPLES
1 x 250
SAMPLES
PREDICTED RATING

## Slide 26
EMBEDDED EEG PRE-PROCESSING
TENSORFLOW GRAPH
A bit more of more detail
HR
EDA
EEG
CH1
CH2
CH3
CH4
CH5
CH6
500 Hz
RAW
UPSAMPLED
125 Hz
UPSAMPLED
125 Hz
6 x 1000
SAMPLES
1 x 250
SAMPLES
1 x 250
SAMPLES
PREDICTED RATING
PER CHANNEL
NORMALIZATION
USING TRAINING-SET STATISTICS
PER CHANNEL
NORMALIZATION
USING TRAINING-SET STATISTICS
PER CHANNEL
NORMALIZATION
USING TRAINING-SET STATISTICS
EEGNet
Lawhern et al. (2018)
8 INPUT CHANNELS
5 OUTPUT CLASSES
1 x 250
SAMPLES
1 x 250
SAMPLES
6 x 250
SAMPLES

## Slide 27
TRAINING SET
TRAINING SET
TRAINING SET
TEST SET
TEST SET
TEST SET
TEST ACCURACY
33.3 %
BATCH SIZE: 128
ITERATIONS: 1000
VALIDATION: 10%
MODEL TRAINING & EVALUATION
DEPLOYMENT
Final model exported as a .tflite file, ready for on-device inference via the Foodback app.

## Slide 28
A TEMPTING ATTEMPT
Epoch-Level Split
80/20 split applied randomly across 2-second epochs
TEST ACCURACY
73.3 %
But too sweet to trust
Why it’s misleading:
Model may memorize session-specific noise or context
Information leakage from overlapping sessions
Overestimates real-world performance

## Slide 29
EVALUATION PROTOCOL
~1 Hz
~10 Hz
500 Hz
Upsampling
Raw Data
Ch1
Ch2
Ch3
Ch4
Ch5
Ch6
The evaluation phase captures 2-second samples
SAMPLES 6x1000
SAMPLES
250
SAMPLES
250
Predicted Rating

## Slide 30
EVALUATION PROTOCOL
(2)
Health check on devices status
Preparation phase of 5 secs
Data collection and model prediction for 2 secs
Score prediction

## Slide 31
FUTURE WORK
To enhance model accuracy and generalizability, future work should include data collection from a larger and more diverse population
A key future goal is to enhance the application to automate the full review process and exploring richer output formats (e.g. free-text review generation)

## Slide 32
CONCLUSIONS
Just a Prototype
Technical viability of real-time, on-device inference
Observed classification performance reflects the true complexity of decoding human taste perception

## Slide 33
What if a single could speak for itself now?
bite
byte

## Slide 34
What if a single could speak for itself now?
byte
Thanks for your attention